## Slide 1: Functional connectivity methods
Iain Stitt

## Slide 2: But first……… our first two-photon imaging!
* Stuber lab mouse

## Slide 3
* Stuber lab mouse

## Slide 4: Functional connectivity methods
Iain Stitt

## Slide 5
A simple case…
Variables:
- Phase
- Amplitude
What to do?
Notes: We record two brain signals (EEG or LFP)
Filter them in a desired frequency band – when looking by eye they appear to be synchronous.
What to do?
Get the analytic representation of the signal by computing the Hilbert transform (or wavelet)
The analytic signal has both real and complex (imaginary) components, and we can use it to extract instantaneous phase and amplitude

## Slide 6: Methods that quantify different kinds of functional connectivity:
Phase locking value (Just phase)
Coherence (Phase and amplitude)
Phase slope index (based on coherence)
Amplitude envelope correlation (Just amplitude)

## Slide 7
Phase locking value (PLV)
Project the phase (or difference in phase) of each observation onto a unit circle
PLV is then defined as the length of the mean of all unit vectors
Matlab
Intuitively
Mathematically

## Slide 8
PLV is dependent on the number of observations used
Underlying distribution

## Slide 9
When comparing groups and conditions you must use the same number of observations to compute PLV (otherwise results are meaningless)
PLV is biased towards 1 with few observations, and 0 with many observations

## Slide 10
Back to our example…

## Slide 11
Coherence
Intuitively
Mathematically
Matlab

## Slide 12
Coherence
“ Phase synchrony is indeed a clearer measure of the phase relationship only, and if is statistically independent of the amplitudes, there is no reason to weight with respect to amplitudes. However, the question is whether this is the case, and, if not, whether the weights result in statistically more robust estimators of phase relationships. “
* Nolte et al 2004
If amplitudes == 1, then coherence reduces to phase locking value
However, some have argued that weighting phase differences with amplitude leads to more robust measures of interaction:

## Slide 13
“ Also, one could argue, in the case of coherence, that assigning a stronger weight to observations with a large amplitude product, one is favoring those observations that have a higher quality phase difference estimate. This realistically assumes that a higher amplitude reflects a higher SNR of the sources of interest and thus, a better quality phase estimate. “
* Bastos & Schoffelen 2016
Coherence

## Slide 14
In the case of clean, artifact-free recordings coherence should be favored.
However, with electrophysiology it is very often the case that we have artifacts (both physiological and non-physiological) common to all recording sites.
Weighting by amplitudes disproportionately amplifies the contribution of high amplitude outliers to the estimate of interaction.
Therefore, unless controlling for zero-phase interaction (next slides…) I feel it is safer to use PLV.
Your thoughts?
My view: Coherence vs PLV

## Slide 15
The volume conduction problem:

## Slide 16
We solve this by breaking Coherency down into its real and imaginary components
Real part = zero-phase lagged component
Imaginary part = non zero-phase lagged component
True interaction
Volume conduction

## Slide 17
Phase Slope Index (directed interaction)
Intuitively
Mathematically
Matlab

## Slide 18
Amplitude envelope correlation
The analytic amplitude must be used (not power!)

## Slide 19
Amplitude envelope correlation following orthogonalization
Like coherence, amplitude envelope correlation is very susceptible to volume conduction (especially in EEG)
To control for this, we can compute the part of signal Y that is orthogonal to signal X
Intuitively
Mathematically
Matlab